Several trucks form an automated convoy with the lead truck sending out acceleration, braking and steering signals so the trucks can react accordingly. The communications between the trucks happen through V2V wireless technology.
Each truck needs to use the sensing technologies, such as sensors, Radar, Lidar, laser scanner to control and monitor general state of each truck and GPS to localize position of the trucks.

1. How can the distance to the precedence truck be guaranteed? It is guaranteed by the following actions,
- Applying Desired Acceleration through Wireless communication & Radar
- Maintaining Relative velocity through Radar & Wireless communication
- Maintaining & Calculating Distance through Radar & Camera

 2. What happen in cases of a e.g., communication failure -> is your system robust / still stable?
 In our design the robustness of the system is ensured for two types of failures,
Wireless communication failure - Loss of desired acceleration from the leading truck.
 • Since it is a major failure, it will impact platooning highly.
 • without the wireless communication the platooning will not be continued.
• If the communication lost happens for a following truck, it will not be able to continue platooning. In respect of the lead truck, the whole platoon will stop.
• By applying gradual braking and with proper signalling, the truck will be stopped in the same lane.

Radar failure – Loss of Distance & relative velocity data between the trucks.
• It is a minor failure, when compared with the loss of wireless communication.
 • The loss of distance & relative velocity data can be retrieved from cameras and wireless communication respectively.
• Even with the loss of radar failure, the platooning will continue its work with the help of wireless communication & cameras.